## Slide 1: CS 383
Computer Organization and Programming
CPU Design & Organization

## Slide 2: History of CPU
First true CPU: C4004 by intel 4 bit at 740,000 cycles/second
Next step: 8086 by intel
  16 bit at 10 Mz
  ○ Introduced x86 instruction set
  i386 (intel)
  32 bit (4 GB memory access)
  Pentium Series 64 bit - pushed Gz limits
Core series took over from here i3 i5 i7

## Slide 3: CPU map
CPU’s currently contain billions of transistors
  Moore’s law - Every 12-18 months the number of transistors per inch doubles Running out of time with this rule however
Commonly dual or quad core
Gz wall currently sits around 4 give or take with overclocking
32 bit vs 64 bit is mainly related to amount of maximum memory

## Slide 4: Basic CPU Info
Clock
  Wire that turns on and off at steady rate (Clock speed)
Basic data input and output
  Retrieves info by requesting memory address in RAM, the enable wires prompts the data to be retrieved, which then move to CPU via data bus
  Writes data by doing same order but instead of enable wire, the set wire to send bits out the data bus
Instruction Set
  Load - loads number from Ram to CPU
  Add, Store, compare
  ump or Jump if (big one) - if statement is true,
  requests another address
  Out and In (inputs)

## Slide 5: What Exactly are the steps?
Instruction Fetch
  Retrieve next instruction code from memory
Decode
  Translates instruction for CPU
Execute
  Performs arithmetic or flag operation
Memory Access
  Data retrieved or stored in cache or memory
Write Back
  Output data is stored in register if needed

## Slide 6: Parts of CPU In depth
Program Counter (Instruction Pointer)
  Holds address of next instruction once current is completed
Accumulator
  Stores results from calculations
Registers
  Super fast storage that stores in the magnitude of bytes
  In CPU and very close to ALU and key components for quick access
Memory Address Register
  Address of data or instruction that is needed
Memory Data Register
  Essentially the buffer of input and output data between CU and rest of CPU/memory
Memory Buffer Register
  Stores data coming or going from memory

## Slide 7: Parts of CPU In depth

## Slide 8: Control Unit
Takes instructions from RAM and translates to instructions for CPU parts
Hardwired
  Enable for retrieving data and writing to bus
Instruction Address Register
  stores location of next instruction
Interrupt processing
  Allows for priority events to jump to the front and interrupt current process

## Slide 9: Arithmetic Logic Unit (ALU)
Receives 2 numbers from registers and performs operation specified by Control Unit
Outputs either arithmetic answer or flag if the numbers were compared
Opcode is the bus that inputs the instructions for the operation
● Status
  Extra information about output
  ○Overflow, carry, or zero
  ●

## Slide 10: Limitations
It only gets so small
Transistors have been getting smaller and smaller but eventually the laws of physics will make it impossible to go any smaller
Current architectures sit at generally 14 nanometer
Past generations were 32 and 22 and not 14 nanometer, getting closer to the wall of 5 nm
What do we do?
What do we do?

## Slide 11: Going Extreme to the Future
Spintronics
  Instead of relying on electron charge, rely on spin direction of electrons
  Much more energy efficient and would make cooler CPU’s
Quantum Computer
  Extremely trivial at the current time BUT
  In theory would exponentially speed up certain calculation

## Slide 12: The Little Man Computer

## Slide 13: Instruction Cycle
Fetch: Little Man finds out what instruction he is to execute
Execute: Little Man performs the work.
1. Little Man reads the address from the location counter
2. He walks over to the mailbox that corresponds to the location counter

## Slide 14: Fetch, cont.
3. And reads the number on the slip of paper (he puts the slip back in case he needs to read it again later)

## Slide 15: Execute Portion
1. The Little Man goes to the mailbox address specified in the instruction he just fetched.
2. He reads the number in that mailbox (he remembers to replace it in case he needs it later).

## Slide 16: Execute, cont.
3. He walks over to the calculator and punches the number in.
4. He walks over to the location counter and clicks it, which gets him ready to fetch the next instruction.

## Slide 17: Address vs. Content
Addresses are consecutive starting at 00 and ending at 99
Content may be
  Data, a three digit number, or
  Instructions
Address | Content

## Slide 18: Instructions
Op code (Operation code)
  In LMC, represented by a single digit Operation code
Operand
  In LMC, represented by two digits following the op code
  Object to be manipulated
    Data or
    Address of data
Address | Content | 
 | Op code | Operand

## Slide 19: Assembly Language
Specific to a CPU
1 to 1 correspondence between assembly language instruction and binary (machine) language instruction
Mnemonics (short character sequence) represent instructions
  Used when programmer needs precise control over hardware, e.g., device drivers

## Slide 20: LMC Architecture
LMC 1.2
LMC 1.3
LMC 1.2: http://community.dur.ac.uk/m.j.r.bordewich/LMC.html
LMC 1.3: http://peterhigginson.co.uk/LMC/

## Slide 21: LMC Instruction Set
LMC 1.2
LMC 1.3

## Slide 22: Instruction Set
Arithmetic | 1xx | ADD
 | 2xx | SUB
Data Movement | 3xx | STORE
 | 5xx | LOAD
Input/Output | 901 | INPUT
 | 902 | Output
Machine Control (coffee break) | 000 | HALT COB

## Slide 23: Input/Output
Move data between calculator and in/out baskets
 |  | Content | 
 |  | Op Code | Operand (address)
IN (input) |  | 9 | 01
OUT (output) |  | 9 | 02

## Slide 24: LMC Input/Output
IN
OUT

## Slide 25: Internal Data Movement
Between mailbox and calculator
 |  | Content | 
 |  | Op Code | Operand (address)
STO (store) |  | 3 | xx
LDA (load) |  | 5 | xx

## Slide 26: LMC Internal Data
LDA
STO

## Slide 27: Arithmetic Instructions
Read mailbox
Perform operation in the calculator
 |  | Content | 
 |  | Op Code | Operand (address)
ADD |  | 1 | xx
SUB |  | 2 | xx

## Slide 28: LMC Arithmetic Instructions
ADD
SUB

## Slide 29: Load and add 2 numbers
INP
STA 99
INP
ADD 99
OUT

## Slide 30: Data storage location
Physically identical to instruction mailbox
Identified by DAT mnemonic
INP ; input first number
STA 06 ; save in memory
INP ; input second number
ADD 06 ; add first number
OUT ; output sum
DAT 942 ; initialize memory with junk

## Slide 31: CPU
Registers is a small amount of Storage available as part of the CPU
FLAGS or Status Register

## Slide 32: Program Control
Branching (executing an instruction out of sequence)
  Changes the address in the Counter
 |  | Content | 
 |  | Op Code | Operand (address)
BR (Jump) |  | 6 | xx
BRZ (Branch on 0) |  | 7 | xx
BRP (Branch on +) |  | 8 | xx

## Slide 33: Branching
BRANCH Always
Set the contents of the accumulator (calculator) to the given address.
BRANCH if ZERO
If the contents of the accumulator (calculator) are 000, the PC (program counter) will be set to the given address.
BRANCH IF ZERO OR POSITIVE
If the contents of the accumulator (calculator) are 000 or positive (i.e. the negative flag is not set), the PC (program counter) will be set to the given address.
FLAGS or Status Register

## Slide 34: LMC Instruction Set
Arithmetic | 1xx | ADD
 | 2xx | SUB
Data Movement | 3xx | STORE
 | 5xx | LOAD
BR | 6xx | JUMP
BRZ | 7xx | BRANC ON 0
BRP | 8xx | BRANCH ON +
Input/Output | 901 | INPUT
 | 902 | OUTPUT
Machine Control (coffee break) | 000 | HALT COB

## Slide 35: Making decisions
Output the largest of two input values.
BRP
5
7
7-5 =2 -> 1
7
5
5-7= -2-> -1

## Slide 36: Write this program using LMC
Output the largest of two input values.
BRP
5
7
7-5 =2 -> 1
7
5
5-7= -2-> -1

## Slide 37: Solution
IN
STO FIRST
IN
STO SECOND
SUB FIRST
BRP SECONDBIG
LDA FIRST
OUT
BR PROGRAMEND
SECONDBIG LDA SECOND
OUT
PROGRAMEND HLT
FIRST DAT
SECOND DAT
INP
STA FIRST
INP
STA SECOND
SUB FIRST
BRP SECONDBIG
LDA FIRST
OUT
BRA PROGRAMEND
SECONDBIG LDA SECOND
OUT
PROGRAMEND HLT
FIRST DAT
SECOND DAT
LMC 1.2
LMC 1.3

## Slide 38: Implementing loops
The following is the flowchart for a program that will output the values from 1 to 10.

## Slide 39: Write this program in LMC
The following is the flowchart for a program that will output the values from 1 to 10.

## Slide 40: Solution
LDA ONE
STO COUNT
OUT
LOOPTOP LDA COUNT
ADD ONE
OUT
STO COUNT
SUB TEN
BRP ENDLOOP
BR LOOPTOP
ENDLOOP HLT
ONE DAT 001
TEN DAT 010
COUNT DA
LDA ONE STA COUNT
OUT LOOPTOP LDA COUNT ADD ONE OUT STA COUNT SUB TEN BRP ENDLOOP BRA LOOPTOP ENDLOOP HLT ONE DAT 001 TEN DAT 010 COUNT DAT
LMC 1.2
LMC 1.3

## Slide 41: LMC Instruction Set
LMC 1.2
LMC 1.3

## Slide 42: Quiz
The triangular numbers are as follows:
1 = 1
3 = 1 + 2
6 = 1 + 2 + 3
10 = 1 + 2 + 3 + 4
15 = 1 + 2 + 3 + 4 + 5
21 = 1 + 2 + 3 + 4 + 5 + 6
etc.
The series begins with 1 (the first triangular number).
To calculate the nth triangular number, n is added to the previous triangular number.
For example, the fourth triangular number is calculated by adding 4 to the third triangular number (which is 6), i.e. 10 = (1 + 2 + 3) + 4.
Write a program that takes a single value (greater or equal to zero) as input and outputs which triangular number it is or 0 if it is not a trinangular number.
For example, if the input is 15, the output will be 5 (15 is the 5th triangular number); and if the input is 7, the output will be 0 (7 is not a triangular number).

## Slide 43: Triangular numbers - Flowchart