## Slide 1: CS 383
Computer Organization and Programming
CPU Design & Organization

## Slide 2: Presentations
Introduction (1 slide)
Background (1 slide)
Main topic (~10-15 slides)
Limitations or Issues of the technology (1 slide)
Current and Future Research topics (1 slide)
Question for Discussion (1 slide)

## Slide 3: Arithmetic calculation
AVR code for z  2x  xy  x2
  Assume that all numbers are 8-bit unsigned
  For x, y, z use registers r16, r17, and r18.

## Slide 4: Arithmetic calculation
AVR code for z  2x  xy  x2
  Assume that all numbers are 8-bit unsigned
  For x, y, z use registers r16, r17, and r18.
.include "m325Pdef.inc"
Main:
ldi r16,$15
ldi r17,$3
ldi r18,0X23
ldi r19, 2
mul r19,r16
mov r20,r0
mul r16,r17
sub r20,r0
mul r16,r16
sub r20,r0
mov r21,r20

## Slide 5: Execution Time
Compute the execution time for the following code snippet:
ldi r16, 0xff
ldi r17, 0xee
add r17, r16
mov r20, r17
Execution Time = (4)/(16MHz) = 0.26μsec
MegaHertZ (MHz) One million cycles per second.
A one-megahertz clock (1 MHz) means some number of bits can be manipulated at least one million times per second.

## Slide 6: Execution Time ?
;Col_1
Col_2 Col_3 Col_4
Begin: |  |  |  |  | 
 | add | R16, | R17 | ; | Add R17 into R16
 | dec | R17 |  | ; | Decrement the value contained in R17
 | mov | R18, | R16 | ; | Copy the value in R16 to R18
END: | jmp | END |  | ; | Jump to the label END
Execution time for 1 complete loop ???

## Slide 7: Data representation
Hex numbers
  0x or 0X
  Put $ in front of the number
Binary numbers
  0b10011001
Decimal numbers
  Just the number
ASCII numbers
  ‘9’
LDI R16, 0x99
LDI R16, $22
LDI R16, 0b10011001
LDI R16, 6
LDI R16, ‘9’

## Slide 8: Assembly directives
An assembly program can include directives
For symbol definitions
  All symbols used in a program will be replaced by the real values when assembling
For program and data organization
  .org, .cseg, .dseg
For data/variable memory allocation
  .db, .dw

## Slide 9: Assembly directives
Define an alias for a register
.def temp = r15
Define symbols for values
.equ length = 2
  Once set, the symbol cannot be redefined to other value later in the program
Define symbols for values
.set input = 5
  The symbol can be changed to represent other values later in the program.

## Slide 10: Program/data memory organization
AVR has three different memories
  Program memory – instructions
  Data memory – variable data
  EEPROM memory – non- volatile data memory
Memory segment directives specify which memory segment to use
  .dseg - Data segment
  .cseg - Code segment
  .eseg - EEPROM segment

## Slide 11: Constants & Variables
Specify the memory locations/sizes for:
  Constants - In program/EEPROM memory
  Variables - In data memory
Store data in program/EEPROM memory
.db - Store byte constants
.dw - Store word (16-bit) constants
Reserve bytes in data memory
.byte - Reserve a number of bytes for a variable

## Slide 12: Program/data memory organization
.dseg ; Start data segment
vartab: .byte 4 ; Reserve 4 bytes in SRAM
.cseg ; Start code segment
; default start location is 0x0000
as: .db 'C'
const: .dw 10, 0x10, 0b10, -1
; Write 10, 16, 2, -1 in program
; memory, each value takes
; 2 bytes.

## Slide 13: CLR – Clear Register
Clears a register. This instruction performs an Exclusive OR between a register and itself. This will clear all bits in the register.
Operation:
Rd ← Rd ⊕ Rd
Program Counter:
PC ← PC + 1
Example:
clr r16

## Slide 14: SER – Set all Bits in Register
Loads $FF directly to register Rd.
Operation:
(i) Rd ← $FF
Program Counter:
PC ← PC + 1
Example:
ser r17

## Slide 15: NOP – No Operation
This instruction performs a single cycle No Operation.
Operation:
Program Counter:
PC ← PC + 1
Example:
nop

## Slide 16: Status Register
I | T | H | S | V | N | Z | C
Global Interrupt Enable/ Disable
Transfer bit used
Half Carry Flag
For signed tests
complement overflow indicator
Negative Flag
Zero Flag
Carry Flag

## Slide 17: Status flags
Add the numbers :
  $38 + $2F
  $9C + $64
  $88 + $ 93
Load 4 to a register
  Decrease 4 times

## Slide 18
Conditional Branching
1

## Slide 19: Control Structure
IF-THEN-ELSE control structure
Numbers x, z are 8-bit integers and stored in registers. You need to decide which registers to use.
Instructions interested
  Compare
  Conditional branch
  Unconditional jump
if (a < 0)
b = 1;
else
b = 3;

## Slide 20: Compare
Syntax:
Operands:
Operation:
cp Rd, Rr
Rd {r0, r1, …, r31}
Rd–Rr
Flags affected: H, S, V, N, Z, C
1
1
; Compare r4 with r5
; Branch if r4  r5
Words:
Cycles:
Example:
cp r4, r5 brne noteq
...
noteq: nop
; Branch destination (do nothing)

## Slide 21: Compare with Immediate
cpi Rd, k
Rd {r16, r17, …, r31} and 0
Syntax:
Operands:
k  255
Operation:
Rd – k
Flags affected: H, S, V, N, Z, C
Words:
Cycles:
1
1
This instruction performs a compare between register Rd and a constant.
cpi r19,3 ; Compare r19 with 3
brne error ; Branch if r19⇔3 ...
error: nop ; Branch destination (do nothing)

## Slide 22
BREQ - Branch if Equal
BRNE - Branch if Not Equal
BRGE - Branch if Greater or Equal Signed)
BRLO - Branch if Lower (Unsigned)

## Slide 23: Conditional Branch
Syntax:
Operands:
Operation:
brge k
-64 ≤ k < 64
If RdRr (NV=0) then PCPC+k+1, else PC  PC+1 if condition is false
Flag affected: None
Words:
Cycles:
1
1 if condition is false; 2 if condition is true
Branch if Greater or Equal Signed)
cp r11,r12 ; Compare registers r11 and r12
brge greateq ; Branch if r11 ≥ r12 (signed)
...
greateq: nop ; Branch destination (do nothing)

## Slide 24: Jump
Syntax:
Operands:
Operation:
jump k
PC ← k
JMP k 0 ≤ k < 4M PC ← k Unchanged
Flag affected: None
Words:
Cycles:
2
3
mov r1,r0 ; Copy r0 to r1
jmp farplc ; Unconditional jump
...
farplc: nop ; Jump destination (do nothing)

## Slide 25: Relative Jump
Syntax:
Operands:
Operation:
rjmp k
-2K ≤ k < 2K PC  PC+k+1
Flag affected: None
Words:
Cycles:
1
2
cpi r16,$42 ; Compare r16 to $42
brne error ; Branch if r16 ⇔ $42
rjmp ok ; Unconditional branch
error: addr16,r17 ; Add r17 to r16
incr16 ; Increment r16
ok: nop ; Destination for rjmp (do nothing)

## Slide 26: Control
IF-THEN-ELSE control structure
Numbers x, z are 8-bit signed integers and stored in registers. You need to decide which registers to use.
.def .def | a = b = cpi | r16 r17 a, 0 | ; | a - 0 | 
 | brge | ELSE | ; | if a  | 0
 | ldi | b, 1 | ; | b = 1 | 
 | rjmp | END | ; | end of | IF statement
ELSE: | ldi | b, 3 | ; | b = 3 | 
END: | … |  |  |  | 61
if (a < 0)
b = 1;
else
b = 3;

## Slide 27: Ports

## Slide 28: AVR Registers (cont.)
General purpose registers
  The following register pairs can work as address
indexes
 X, r26:r27
 Y, r28:r29
 Z, r30:r31
  The following registers can be applied for specific
use
    r1:r0 store the result of multiplication instruction
    r0 stores the data loaded from the program memory

## Slide 29: OUT
Stores data from register Rr in the Register File to I/O Space (Ports, Timers, Configuration Registers etc.).
Operation:
I/O(A) ← Rr
Program Counter:
PC ← PC + 1
Example:
clr r16 ser r17 out $18,r16
nop out $18,r17

## Slide 30: IN - Load an I/O Location to Register
Loads data from the I/O Space (Ports, Timers, Configuration Registers etc.) into register Rd in the Register File.
Operation:
Rd ← I/O(A)
Program Counter:
PC ← PC + 1
Example:
in r16, PinD

## Slide 31: Port Registers
PORTD maps to Arduino digital pins 0 to 7
  DDRD - The Port D Data Direction Register - read/write
  PORTD - The Port D Data Register - read/write
  PIND - The Port D Input Pins Register - read only
PORTB maps to Arduino digital pins 8 to 13 The two high bits (6 & 7) map to the crystal pins and are not usable
  DDRB - The Port B Data Direction Register - read/write
  PORTB - The Port B Data Register - read/write
  PINB - The Port B Input Pins Register - read only
PORTC maps to Arduino analog pins 0 to 5. Pins 6 & 7 are only accessible on the Arduino Mini
  DDRC - The Port C Data Direction Register - read/write
  PORTC - The Port C Data Register - read/write
  PINC - The Port C Input Pins Register - read only
Each bit of these registers corresponds to a single pin; e.g. the low bit of DDRB, PORTB, and PINB refers to pin PB0(digital pin 8)

## Slide 32: Input and Output
.include "m328Pdef.inc"
Init:
ser r16
out DDRB, r16
ldi r16, 0b11111110
out DDRD, r16
clr r16
out PortB, r16
ldi r16, 0b00000001
out PortD, r16
Main:
in r16, PinD
out PortB, r16
rjmp Main
We use the last bit of D as input
We use the whole bits of B as output
For the first run of the code, nothing happened.
PortB and PortD should look like this:
Prefix 0b followed by a series of 0 and 1digits, e.g. 0b11 == 3.
Constants B0 through B11111111

## Slide 33: Input and Output
.include "m328Pdef.inc"
Init:
ser r16
out DDRB, r16
ldi r16, 0b11111110
out DDRD, r16
clr r16
out PortB, r16
ldi r16, 0b00000001
out PortD, r16
Main:
in r16, PinD
out PortB, r16
rjmp Main
We use the last bit of D as input
We use the whole bits of B as output
For the first run of the code, nothing happened.
PortB and PortD should look like this:

## Slide 34: Input and Output
.include "m328Pdef.inc"
Init:
ser r16
out DDRB, r16
ldi r16, 0b11111110
out DDRD, r16
clr r16
out PortB, r16
ldi r16, 0b00000001
out PortD, r16
Main:
in r16, PinD
out PortB, r16
rjmp Main
When the code runs to the point “rjmp Main”, click the last bit of the PIND to light up the bit as an input:

## Slide 35: Input and Output
.include "m328Pdef.inc"
Init:
ser r16
out DDRB, r16
ldi r16, 0b11111110
out DDRD, r16
clr r16
out PortB, r16
ldi r16, 0b00000001
out PortD, r16
Main:
in r16, PinD
out PortB, r16
rjmp Main
then continue to execute the program, you can see that the r16 register becomes 1, which means it reads the bit we modified, then you can see the last bit of PortB lights up.