## Slide 1: CS 383
Computer Organization and Programming
Loops

## Slide 2: Using register Z
Write an assembly language program that gets the numbers from the Data Space with memory address 0x0100. Use register z to get number.
.include "m325Pdef.inc”
init:
ldi r22, 0x20
sts 0x0100, r22
main:
ldi zh, 0x01
ldi zl, 0x00
clr r22
ld r22, z

## Slide 3: Branching

## Slide 4: Relevant Instructions
brne – Branch if not equal
breq – Branch if equal
brlt – Branch if less than
brge – Branch if greater than or equal
cp – Compare
cpi – Compare with immediate
jmp – Jump

## Slide 5: Exercise 1
Find the maximum of two numbers stored in r16 and r17. Store the answer in r18.

## Slide 6: Exercise 1 (Solution)
main:
cp r16,r17 ; compare values in r16 and r17
brge r16_greater ; if r16 is greater or equal, jump to label
mov r18,r17 ; copy value from r17 to r18
rjmp end ; jump to end
r16_greater:
mov r18,r16 ; copy value from r16 to r18
end:
ret ; return

## Slide 7: Schedule
Assembly Assignment – Thursday 13
Assembly Exam 1 exercise – Tuesday 18
Midterm – Friday 21 Oct

## Slide 8: Loops
// C code example
int i = 1;
int sum = 0;
while (i <= 10)
{
sum = sum + i;
i = i + 1;
}
; AVR Assembly example
.def i = r16
.def sum = r17
main:
ldi i,1 ; i = 1
ldi sum,0 ; sum = 0
rjmp loop ; jump to loop
loop:
add sum,i ; sum = sum + i
cpi i,10 ; compare i and 10
breq end ; if i == 10, jump to end
inc i ; increment i
rjmp loop ; jump to top of loop
end:
ret ; return

## Slide 9: Exercise 2
Write an assembly language program to find the largest number in 5 binary numbers read from Data Space. Get the numbers from the Data Space starts from 0x0100. (use register z to get number)
ld r16, z+ ; load Z into r16, then increment Z

## Slide 10: Exercise 2 (Solution)
.include "m328Pdef.inc"
main:
ldi zh, 0x01
ldi zl, 0x00
ldi r20, 0x14
clr r21
loop:
ld r16, z+
cp r21, r16
brsh continue
mov r21, r16
continue:
dec r20
cpi r20, 0
breq end
rjmp loop
end:
move r22,r21