## Slide 1
Quiz
1

## Slide 2: Execution Time
Compute the execution time for the following code snippet:
.include "m328Pdef.inc”
Init:
ser r16
out DDRB,r16
ldi r16,0b11111110
out DDRD,r16
clr r16
out PortB, r16
ldi r16,0b00000001
out PortD, r16
Main:
in r16, PinD
out PortB, r16
rjmp Main

## Slide 3
Arduino Port Registers
1

## Slide 4: Port Registers
PORTD maps to Arduino digital pins 0 to 7
  DDRD - The Port D Data Direction Register - read/write
  PORTD - The Port D Data Register - read/write
  PIND - The Port D Input Pins Register - read only
PORTB maps to Arduino digital pins 8 to 13 The two high bits (6 & 7) map to the crystal pins and are not usable
  DDRB - The Port B Data Direction Register - read/write
  PORTB - The Port B Data Register - read/write
  PINB - The Port B Input Pins Register - read only
PORTC maps to Arduino analog pins 0 to 5. Pins 6 & 7 are only accessible on the Arduino Mini
  DDRC - The Port C Data Direction Register - read/write
  PORTC - The Port C Data Register - read/write
  PINC - The Port C Input Pins Register - read only
Each bit of these registers corresponds to a single pin; e.g. the low bit of DDRB, PORTB, and PINB refers to pin PB0(digital pin 8)

## Slide 5: CLR – Clear Register
Clears a register. This instruction performs an Exclusive OR between a register and itself. This will clear all bits in the register.
Operation:
Rd ← Rd ⊕ Rd
Program Counter:
PC ← PC + 1
Example:
clr r16

## Slide 6: SER – Set all Bits in Register
Loads $FF directly to register Rd.
Operation:
(i) Rd ← $FF
Program Counter:
PC ← PC + 1
Example:
ser r17

## Slide 7: NOP – No Operation
This instruction performs a single cycle No Operation.
Operation:
Program Counter:
PC ← PC + 1
Example:
nop

## Slide 8: OUT
Stores data from register Rr in the Register File to I/O Space (Ports, Timers, Configuration Registers etc.).
Operation:
I/O(A) ← Rr
Program Counter:
PC ← PC + 1
Example:
clr r16 ser r17 out $18,r16
nop out $18,r17

## Slide 9: IN - Load an I/O Location to Register
Loads data from the I/O Space (Ports, Timers, Configuration Registers etc.) into register Rd in the Register File.
Operation:
Rd ← I/O(A)
Program Counter:
PC ← PC + 1
Example:
in r16, PinD

## Slide 10: Input and Output
.include "m328Pdef.inc"
Init:
ser r16
out DDRB, r16
ldi r16, 0b11111110
out DDRD, r16
clr r16
out PortB, r16
ldi r16, 0b00000001
out PortD, r16
Main:
in r16, PinD
out PortB, r16
rjmp Main
We use the last bit of D as input
We use the whole bits of B as output
For the first run of the code, nothing happened.
PortB and PortD should look like this:
Prefix 0b followed by a series of 0 and 1digits, e.g. 0b11 == 3.
Constants B0 through B11111111

## Slide 11: Input and Output
.include "m328Pdef.inc"
Init:
ser r16
out DDRB, r16
ldi r16, 0b11111110
out DDRD, r16
clr r16
out PortB, r16
ldi r16, 0b00000001
out PortD, r16
Main:
in r16, PinD
out PortB, r16
rjmp Main
We use the last bit of D as input
We use the whole bits of B as output
For the first run of the code, nothing happened.
PortB and PortD should look like this:

## Slide 12: Input and Output
.include "m328Pdef.inc"
Init:
ser r16
out DDRB, r16
ldi r16, 0b11111110
out DDRD, r16
clr r16
out PortB, r16
ldi r16, 0b00000001
out PortD, r16
Main:
in r16, PinD
out PortB, r16
rjmp Main
When the code runs to the point “rjmp Main”, click the last bit of the PIND to light up the bit as an input:

## Slide 13: Input and Output
.include "m328Pdef.inc"
Init:
ser r16
out DDRB, r16
ldi r16, 0b11111110
out DDRD, r16
clr r16
out PortB, r16
ldi r16, 0b00000001
out PortD, r16
Main:
in r16, PinD
out PortB, r16
rjmp Main
then continue to execute the program, you can see that the r16 register becomes 1, which means it reads the bit we modified, then you can see the last bit of PortB lights up.

## Slide 14
Conditional Branching
1

## Slide 15: Control Structure
IF-THEN-ELSE control structure
Numbers x, z are 8-bit integers and stored in registers. You need to decide which registers to use.
Instructions interested
  Compare
  Conditional branch
  Unconditional jump
if (a < 0)
b = 1;
else
b = 3;

## Slide 16: Compare
Syntax:
Operands:
Operation:
cp Rd, Rr
Rd {r0, r1, …, r31}
Rd–Rr
Flags affected: H, S, V, N, Z, C
1
1
; Compare r4 with r5
; Branch if r4  r5
Words:
Cycles:
Example:
cp r4, r5 brne noteq
...
noteq: nop
; Branch destination (do nothing)

## Slide 17: Compare with Immediate
cpi Rd, k
Rd {r16, r17, …, r31} and 0
Syntax:
Operands:
k  255
Operation:
Rd – k
Flags affected: H, S, V, N, Z, C
Words:
Cycles:
1
1
This instruction performs a compare between register Rd and a constant.
cpi r19,3 ; Compare r19 with 3
brne error ; Branch if r19⇔3 ...
error: nop ; Branch destination (do nothing)

## Slide 18
BREQ - Branch if Equal
BRNE - Branch if Not Equal
BRGE - Branch if Greater or Equal Signed)
BRLO - Branch if Lower (Unsigned)

## Slide 19: Conditional Branch
Syntax:
Operands:
Operation:
brge k
-64 ≤ k < 64
If RdRr (NV=0) then PCPC+k+1, else PC  PC+1 if condition is false
Flag affected: None
Words:
Cycles:
1
1 if condition is false; 2 if condition is true
Branch if Greater or Equal Signed)
cp r11,r12 ; Compare registers r11 and r12
brge greateq ; Branch if r11 ≥ r12 (signed)
...
greateq: nop ; Branch destination (do nothing)

## Slide 20: Jump
Syntax:
Operands:
Operation:
jump k
PC ← k
JMP k 0 ≤ k < 4M PC ← k Unchanged
Flag affected: None
Words:
Cycles:
2
3
mov r1,r0 ; Copy r0 to r1
jmp farplc ; Unconditional jump
...
farplc: nop ; Jump destination (do nothing)

## Slide 21: Relative Jump
Syntax:
Operands:
Operation:
rjmp k
-2K ≤ k < 2K PC  PC+k+1
Flag affected: None
Words:
Cycles:
1
2
cpi r16,$42 ; Compare r16 to $42
brne error ; Branch if r16 ⇔ $42
rjmp ok ; Unconditional branch
error: addr16,r17 ; Add r17 to r16
incr16 ; Increment r16
ok: nop ; Destination for rjmp (do nothing)

## Slide 22: Control
IF-THEN-ELSE control structure
Numbers x, z are 8-bit signed integers and stored in registers. You need to decide which registers to use.
.def .def | a = b = cpi | r16 r17 a, 0 | ; | a - 0 | 
 | brge | ELSE | ; | if a  | 0
 | ldi | b, 1 | ; | b = 1 | 
 | rjmp | END | ; | end of | IF statement
ELSE: | ldi | b, 3 | ; | b = 3 | 
END: | … |  |  |  | 61
if (a < 0)
b = 1;
else
b = 3;

## Slide 23: AVR Registers (cont.)
General purpose registers
  The following register pairs can work as address
indexes
 X, r26:r27
 Y, r28:r29
 Z, r30:r31
  The following registers can be applied for specific
use
    r1:r0 store the result of multiplication instruction
    r0 stores the data loaded from the program memory