## Slide 1
  Address Space
1

## Slide 2: Address Space
0x0000 0x0020 | -­‐ -­‐ | 0x001F 0x005F
0x0060 | -­‐ | 0x00FF
0x0100 -­‐ 0x08FF

## Slide 3: X, Y, Z
0x00 | R0 |  | 
0x01 | R1 |  | 
0x02 | R2 |  | 
0x0D | R13 |  | 
0x0E | R14 |  | 
0x0F | R15 |  | 
0x10 | R16 |  | 
0x11 | R17 |  | 
0x1A | R26 | X-register | Low byte
0x1B | R27 | X-register | High byte
0x1C | R28 | Y-register | Low byte
0x1D | R29 | Y-register | High byte
0x1E | R30 | Z-register | Low byte
0x1F | R31 | Z-register | High byte

## Slide 4: LDI - Load Immediate
ldi Rd, k
Rd{r16, …, r31}, 0 ≤ k 
Syntax:
Operands:
255
Operation:
Rdk
Flag affected: None
1
1
1110 kkkk dddd kkkk
Words:
Cycles:
Encoding:
Example:
ldi r16, 0x42
; Load 0x42 to r16
10

## Slide 5: LDS – Load Direct from Data Space
Loads one byte from the data space to a register. For parts with SRAM, the data space consists of the Register File, I/O memory and internal SRAM (and external SRAM if applicable).
Loads one byte from the data space to a register
A 16-bit address must be supplied
lds r2,$FF00 ;Load r2 with the contents of data space location $FF00
add r2,r1 ; add r1 to r2

## Slide 6: STS - Store Direct to data space
Loads one byte from the data space to a register
A 16-bit address must be supplied
lds r2,$FF00 ;Load r2 with the contents of data space location $FF00
add r2,r1 ; add r1 to r2
sts $FF00,r2 ; Write back

## Slide 7: Example 1
Write an assembly language program that gets the numbers from the Data Space with memory address 0x0100.
Output the lower byte of the result to Port B and the high byte of the result to Port C.
Use register z to get number.
.include "m325Pdef.inc”
init:
ldi r22, 0x20
sts 0x0100, r22
main:
ldi zh, 0x01
ldi zl, 0x00
clr r22
ld r22, z
output:
ser r16
out DDRB, r16
out DDRC, r16
out PortB, r30
out PortC, r31
ret