## Slide 1
Introduction to Arduino

## Slide 2: Arduino Uno – Compatibles

## Slide 3: Hardware & Software
Software
Arduino IDE
• C/C++
ASM

## Slide 4: Introduction to Assembly
Oldest non-machine language
Assembly is close to a one to one correspondence between symbolic instructions and executable machine codes
Assembly gives access to key machine features for low-level routines (OS kernel, microkernel, device drivers, machine control...)
High quality assembly can be 2 to 20 times faster

## Slide 5: C can be close to assembly
Both can:
Access all the functions/ registers of the ATMega328
Have a decidedly smaller footprint than Arduino code.
In Assembly…
working with the program counter and the stack.
no predefined data types
working directly with addresses or pointers

## Slide 6: Software Comparison
 | Arduino IDE | C/C++ | ASM
Ease of Development | Easy | Moderate | Challenging
Libraries | Many | Many | None
Speed | SLOW | Fast | FAST as Possible
Accessibility of processor features | Very Limited | Most | ALL

## Slide 7
Overview of the ATMega328

## Slide 8: ATMega328 Internals
PORT C
PORT B
PORT D
USART 0
16bit T/C 1
8bit T/C 0
8bit T/C 2
A/D Convertor
Internal Bandgap
Analog Comparator
SPI
TWI
SRAM
Flash
Watchdog Oscillator
Watchdog Timer
Oscillator Circuits/ Clock Generation
VCC
GND
PROGRAM
LOGIC
debugWIRE fuse
2
GND
EEPROM AREF
AVCC
DATABUS
ADC [6..7]
Port C [0..6]
Port B [0..7]
Port D [0..7]
6
7
8
8
RESET
XTAL[1..2]
CPU
Power Supervision POR/BOD & RESET

## Slide 9: Processor Layout

## Slide 10: ATMega328 Ports
Port D
DATABUS
ADC[6..7]
PC[0..6]
PB[0..7]
PD[0..7]
RESET
XTAL[1..2]
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Comp. |  |  |  |  |  |  |  | 
PC6 | 1 | 28 |  | PC5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PD0 PD1 | 2 3 | 27 26 |  | PC4 PC3 | Port C |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PD2 PD3 | 4 5 | 25 24 |  | PC2 PC1 |  |  |  |  |  | USART 0 |  |  |  |  | SPI |  |  |  |  | TWI |  |  | 
PD4 | 6 | 23 |  | PC0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
VCC | 7 | 22 |  | GND |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
GND | 8 | 21 |  | AREF |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PB6 | 9 | 20 |  | AVCC |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PB7 | 10 | 19 |  | PB5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PD5 | 11 | 18 |  | PB4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PD6 | 12 | 17 |  | PB3 | Port B |  |  |  |  | PORT D (8) |  |  |  |  | PORT B (8) |  |  |  |  | PORT C (7) |  |  | 
PD7 | 13 | 16 |  | PB2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PB0 | 14 | 15 |  | PB1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
bidirectional ports

## Slide 11: ATMega328 Features
Low Power AVR 8bit Microcontroller
131 Powerful instructions
32x8 General Purpose Working Registers
  On-chip 2-cycle Multiplier
Non-volatile Memory Segments
  32Kb Self-Programmable Flash program memory
  1Kb EEPROM
  2Kb Internal SRAM

## Slide 12: Arithmetic Logic Unit (ALU)
Directly connected to all 32 general purpose registers
Operations between registers executed within a single clock cycle
Supports arithmetic, logic and bit functions
On-chip 2-cycle Multiplier

## Slide 13: Arduino MCU Register
...
...
...
...
0x00 | R0 |  | 
0x01 | R1 |  | 
0x02 | R2 |  | 
0x0D | R13 |  | 
0x0E | R14 |  | 
0x0F | R15 |  | 
0x10 | R16 |  | 
0x11 | R17 |  | 
0x1A | R26 | X-register | Low byte
0x1B | R27 | X-register | High byte
0x1C | R28 | Y-register | Low byte
0x1D | R29 | Y-register | High byte
0x1E | R30 | Z-register | Low byte
0x1F | R31 | Z-register | High byte

## Slide 14: Memory Mapped I/O Space
I/O registers visible in data space
  I/O can be accessed using same instructions as data
  Compilers can treat I/O space as data access
Bit manipulation instructions
  Set/Clear single I/O bits
  Only work on lower memory addresses

## Slide 15: Memory Map
0x0000 0x0020 | -­‐ -­‐ | 0x001F 0x005F
0x0060 | -­‐ | 0x00FF
0x0100 -­‐ 0x08FF

## Slide 16: I/O Addresses
Address Range |  |  | Purpose
0x0100 | -­‐ | 0x08FF | 2K SRAM (general purpose RAM)
0x0020 | -­‐ | 0x00FF | Memory Mapped I/O
0x0000 | -­‐ | 0x001F | Registers r0 -­‐ r31
I/O Address | Memory Address | Designation |  |  | 
0x03 0x04 0x05 | 0x0023 0x0024 0x0025 | PINB -­‐ DDRB -­‐ PORTB | input, port B data direction, -­‐ output, port B | port | B
0x06 0x07 0x08 | 0x0026 0x0027 0x0028 | PINC -­‐ DDRC -­‐ PORTC | input, port C data direction, -­‐ output, port C | port | C
0x09 0x0A 0x0B | 0x0029 0x002A 0x002B | PIND -­‐ DDRD -­‐ PORTD | input, port D data direction, -­‐ output, port D | port | D

## Slide 17: 131 Instructions
Arithmetic & Logic
Branch
Bit set/clear/test
Data transfer
Microcontroller control

## Slide 18: Instruction Timing
Register -> register (1 cycle)
Register -> memory (2 cycles)
Branch instruction (1-2 cycles)
Subroutine call & return (3-5 cycles)
Some operations may take longer for external memory

## Slide 19: Clock System - Timers/Counters
Clock control module generates clocks for memory and IO devices
Multiple internal clock sources
Default is only 5-10% accurate

## Slide 20: Timers/Counters
8/16 Bit register
  Increments or decrements on every clock cycle
  Can be read on data bus
  Output feeds waveform generator
Clock Sources
  Internal from clock prescaler
  External Tn Pin (Uses 1 port pin)

## Slide 21: Interrupts
ATmega328 has 26 reset/interrupt sources
1 Reset source
2 External interrupt sources
I/O Pin state change on all 24 GPIO pins
Peripheral device events

## Slide 22: AVR Studio/Toolchain
Slick integrated environment (Windows)
Directly incorporates Assembly
Requires knowledge of the bootloading process
For power users.

## Slide 23: Atmel Studio Setup Instructions
Visit the Atmel Studio 6.2 download page at:
http://www.atmel.com/tools/ATMELSTUDIO.aspx
Once, downloaded, run the installer
You may be prompted to download Microsoft Visual Studio Isolated Shell 10.0

## Slide 24: Create a new assembler project
Open Atmel Studio
Click “File” -> “New” -> “Project”, select “Assembler” -> “AVR Assembler Project” and click “OK” to create a new project.
In “Device Selection” Window, choose “ATmega328P” device and click “OK”.

## Slide 25: Setting up the Arduino Assembly
The Arduino IDE doesn’t directly allow assembly
A number of approaches exist to do assembly with the Arduino IDE:
  Modify the IDE
  “Inline” Assembly

## Slide 26: Inline Assembly
Allows for all the assembly commands and structures.
Requires a lot of extra stuff in the code to support the program that is not a part of the program
more difficult to read/debug

## Slide 27: Inline Assembly Example Line
asm("in %0, %1 \n\t” : "=r" (value) : "I" (_SFR_IO_ADDR(PORTD)) );
asm(…) indicates to the IDE that assembly is used
The assembler instruction is defined as a single string constant: "in %0, %1 \n\t”
The list of output operands follow, separated by commas.
"=r" (value)
Next, a comma separated list of input operands.
"I" (_SFR_IO_ADDR(PORTD))

## Slide 28: Assembly
Begin: |  |  |  |  | 
 | add | R16, | R17 | ; | Add R17 into R16
 | dec | R17 |  | ; | Decrement the value contained in R17
 | mov | R18, | R16 | ; | Copy the value in R16 to R18
END: | jmp | Begin |  | ; | Jump to the label END
Column 1 used for labels.
Column 2 used for the instruction/directive
[Column 3 used for operands]
Column 4 used for comments

## Slide 29: Operand Forms
Rd | Destination (& source) register R0-­‐R31 or R16-­‐R31 | 
Rr | Source register R0-­‐R31 | 
b | Bit in the Register file or I/O Register (3-bit constant) | 
s | Bit in the Status Register (3-bit) | 
X,Y,Z | Indirect Address Register (X=R27:R26, Y=R29:R28, Z=R31:R32) | 
K | Constant data | 
k | Constant Address | 
A | I/O location address | 
q | Displacement for direct addressing (6-bit) | 
PC | Program Counter | 

## Slide 30: Operators
Symb | Name | Returns | Priority
! | Logical Not | 1 if the expression is 0, 0 otherwise | 14
~ | Bitwise Not | all bits inverted | 14
-­‐ | unary minus | the arithmetic negation of expression | 14
* | multiplication | the product of the two expressions | 13
/ | division | the integer quotient (1st exp)/(2nd exp) | 13
+ | addition | the sum of the two expressions | 12
-­‐ | subtraction | the difference (1st exp) – (2nd exp) | 12
<< | shift left | the (1st exp) shifted to the left by the (2nd exp) | 11
>> | shift right | the (1st exp) shifted to the right by the (2nd exp) | 11
< | less than | 1 if the (1st exp) is less than the (2nd exp), 0 else | 10

## Slide 31: Operators
Symb | Name | Returns | Priority
<= | less or equal | 1 only if the (1st exp) is less or equal to the (2nd exp) | 10
> | greater than | 1 if the (1st exp) is greater than the (2nd exp), 0 else | 10
>= | greater or equal | 1 only if the (1st exp) is greater or equal to the (2nd exp) | 10
== | equal | 1 if the (1st exp) is equal to the (2nd exp), 0 else | 9
!= | not equal | 1 if the (1st exp) is not equal to the (2nd exp), 0 else | 9
& | bitwise AND | the bitwise AND of two expressions | 8
^ | bitwise XOR | the bitwise XOR of two expressions | 7
¦ | bitwise OR | the bitwise OR of two expressions | 6
&& | logical AND | true only if both operands are true | 5
¦¦ | logical OR | true if either operand is true | 4