## Slide 1
LED & Button & Delay & Interrupt
1

## Slide 2: Using a Led

## Slide 3: sketch_apr14a.s
#include "avr/io.h”
.global loop
.global setup
setup:
ser r16
sts DDRB, r16
ret
loop:
sts PORTB, r16
ret

## Slide 4: Calculating a delay of 1 s
timer:
LDI R17, 32
L1: LDI R18, 200
L2: LDI R19, 250
L3:
NOP
NOP
DEC R19
BRNE L3
DEC R18
BRNE L2
DEC R17
BRNE L1
ret
#include "avr/io.h"
.text
.global setup
.global loop
.global timer
.global again
setup:
ldi r16, 0b00100000
sts DDRB, r16
loop:
ldi r17, 0b00100000
sts PORTB, r17
call timer
ldi r17, 0b00000000
sts PORTB, r17
call timer
jmp loop

## Slide 5: Stack
setup:
ldi r22, 0x20
sts 0x0100, r22 ; load a value to memory address 0100
ldi r17, 0x00
ldi r18, 0x01
mov ZH, r17
mov ZL, r18 ; Z point to memory addres 0100
ldi r16, hi8(RAMEND)
sts SPH, r16
ldi r16, lo8(RAMEND)
sts SPL, r16 ; create the stack
ld r19, Z
; load the value from the memory address that Z register points
push r19 ;push the value to the stack
pop r19 ;pop the value from the stack
LD r28, Z+
; Load the value from the memory address that Z register points, and increase the pointer
loop:
jmp loop
#define __SFR_OFFSET 0
#include "avr/io.h"
#include <avr/portpins.h>
.text
.global setup
.global loop

## Slide 6: Button

## Slide 7: Button and LED – no asm control

## Slide 9: Button and LED –asm control

## Slide 10: Button and LED –asm control

## Slide 11: LED – Button using C
int ledPin = 13; // choose the pin for the LED
int inPin = 7; // choose the input pin (for a pushbutton)
int val = 0; // variable for reading the pin status
void setup() {
pinMode(ledPin, OUTPUT); // declare LED as output
pinMode(inPin, INPUT); // declare pushbutton as input
}
void loop(){
val = digitalRead(inPin); // read input value
if (val == HIGH) { // check if the input is HIGH (button released)
digitalWrite(ledPin, LOW); // turn LED OFF
} else {
digitalWrite(ledPin, HIGH); // turn LED ON
}
}

## Slide 12: LED – Button using assembly
#include "avr/io.h"
.text
.global setup
.global loop
.global one
.global two
setup:
ldi r16, 0b11111111
sts DDRB, r16
ldi r17, 0b00000000
sts DDRD, r16
loop:
one: lds r20, PORTD
cpi r20, 0x00
breq two
sts PORTB, r17
jmp one
two: sts PORTB,r16
jmp one

## Slide 13: LED – Button using assembly
#define __SFR_OFFSET 0
#include "avr/io.h"
#include <avr/portpins.h>
.text
.global setup
.global loop
.global one
.global two
setup:
ldi r16,0b11111111
ldi r17, 0b00000000
ldi r18,0b0100000
out DDRB, r16
out DDRD, r17
loop:
out PORTB, r18
one:
sbis PIND,7
brne two
out PORTB, r17
jmp one
two: out PORTB,r16
jmp one
one: lds r20, PORTD
cpi r20, 0x00
breq two

## Slide 14: AVR Interrupts
An interrupt is a signal to the processor emitted by hardware or software indicating an event that needs immediate attention
An interrupt alerts the processor to a high-priority condition requiring the interruption of the current code the processor is executing.
Basically can be divided into internal and external interrupts
Hardware is used to recognize interrupts

## Slide 15: AVR Interrupts
To enable an interrupt, two control bits must be set
  the Global Interrupt Enable bit (I bit) in the Status Register
    Using sei instruction
  the enable bit for that interrupt
To disable all maskable interrupts, reset the I bit in SREG
  Using cli instruction
Priority of interrupts is used to handle multiple simultaneous interrupts

## Slide 16: Set Global Interrupt Flag - sei
Sets the global interrupt flag (I) in SREG. The instruction following SEI will be executed before any pending interrupts.
sei ; set global interrupt enable
sleep ; enter sleep state, waiting for an interrupt

## Slide 17: Clear Global Interrupt Flag - cli
Clears the Global interrupt flag in SREG. Interrupts will be immediately disabled.
in r18, SREG ; store SREG value
cli ; disable interrupts
; do something very important here out
SREG, r18 ; restore SREG value

## Slide 18: Interrupt Register
External Interrupt Control Register A (EICRA)
External Interrupt Mask Register (EIMSK)

## Slide 19: External Interrupt Mask Register (EIMSK)

## Slide 20: Interrupts
The interrupt execution response for all the enabled AVR interrupts is basically five clock cycles minimum.
  For saving the Program Counter (2 clock cycles)
  For jumping to the interrupt routine (3 clock cycles)
The priority of an interrupt is based on the position of its vector in the program memory
The lower the address the higher is the priority level.
RESET has the highest priority

## Slide 21: LED – Interrupts
#include <avr/interrupt.h>
.text
.global setup
.global loop
.global INT0_vect
setup:
clr r20
// value indicate the pin13 status
clr r16
sts DDRD, r16
// set portD as input
ser r16
sts DDRB, r16
// set portB as output
ldi r16, 0b00100000
sts PORTB, r16
sei
ldi r16, 0b00000001
sts EIMSK, r16
// set interrupt mask as INT0
ldi r16, 0b00000011
sts EICRA, r16
// set the EICRA to response to rising edge of INT0
loop:
rjmp loop
INT0_vect:
lds r20, PORTB
cpi r20, 0x00
breq lightup
clr r16
sts PORTB, r16
reti
lightup:
ldi r16, 0b00100000
sts PORTB, r16
reti